## Slide 1: Mobile and WIRLESS network
(Period-10, Marks 10)

## Slide 2: Wireless network
How Wireless Networks Work
  Radio / Electromagnetic waves
    Similar to physical layer of OSI
  Data Format
    Higher layer of OSI
  Network Structure
    wireless network interface adapters and base stations
  Each of the broadband wireless data services use different combination of radio signals, data formats, and network structure

## Slide 3: Radio Communication : Spectrum

## Slide 5: Wireless data network
Unlicensed radio services
  Wi-Fi networks operate in a special band of radio frequencies around 2.4 -2.5 GHz and 5.725-5.875 GHz
Point-to-Point
  A point-to-point radio service operates a communication channel that carries information from a transmitter to a single receiver
  The opposite of point-to-point is a broadcast service (such as a radio or television station) that sends the same signal to many receivers at the same time

## Slide 6: Wireless Networks

## Slide 7: Wireless data network
Spread Spectrum
  Spread spectrum is a family of methods for transmitting a single radio signal using a relatively wide segment of the radio spectrum

## Slide 8
DSSS
FHSS
OFDM
https://www.youtube.com/watch?v=KCHO7zlU25Q

## Slide 9: Types of Wireless Network
Wireless personal-area networks (WPAN)
  short range (up to 20–30 feet/7–10 meters)
  802.15 family of specifications to connect two or a few devices with low power consumption. Bluetooth is an example of WPAN protocol
Wireless local-area networks (WLAN)
  300 feet (100 meters)
  802.11 family

## Slide 10: Types of Wireless Network
Wireless metropolitan-area network (WMAN)
  Extend the range to a larger geographic area, such as a city or suburb. Applications vary from point-to-point or point-to-multipoint links to multiuser coverage
  WMANs typically use licensed frequencies although implementations in the ISM bands can also be found
  IEEE 802.16 family

## Slide 11: IEEE standards
IEEE specifies working standards for networking
  802.3 Ethernet CSMA/CD
  802.5 Token ring
  802.11 x for wireless LAN
  802.15 for WPAN : Bluetooth and ZeeBi
  802.16 for WiMAx
Basically these specifications used for the product developments and applications
  Data rate ,operating frequency etc

## Slide 12: Wireless topologies
Two wireless devices in range of each other just need to share a common set of simple parameters (frequency and so on) to be able to communicate and establish a WLAN
A first station defines the radio parameters and a connection name; the other stations just need to detect the connection and adjust their own parameters to connect to the first station and to each other. This is called an ad hoc network.

## Slide 13: Ad hoc network
Ad-hoc networks are limited in functionality because no central device is present to decide common rules
radio parameters, priority, range, what happens if the first station disappears, and so on)
wireless network they form is called an Independent Basic Service Set (IBSS)

## Slide 14: Infrastructure Network
To organize the communication, most networks use a central device that defines common sets of parameters: the access point (AP)
relays the signal to the destination wireless station or the wired network
AP is a hybrid device, close to an Ethernet hub in concept : All stations share the same frequency, and only one station can send at any given time

## Slide 15
Infrastructure network
ad-hoc network
AP
AP
AP
wired network
AP: Access Point
Infrastructure and ad-hoc networks
Click to add text

## Slide 16: System architecture 802.11
Infrastructure

## Slide 17: System architecture 802.11
Adhoc Basic Service set
IBSS1
STA1
STA2
STA3

## Slide 18: Protocol architecture and bridging
mobile terminal
access point
application
TCP
802.11 PHY
802.11 MAC
IP
802.3 MAC
802.3 PHY
application
TCP
802.3 PHY
802.3 MAC
IP
802.11 MAC
802.11 PHY
LLC
infrastructure
network
LLC
LLC
Fixed Terminal

## Slide 19: 802.11 - Layers and functions
PLCP Physical Layer Convergence Protocol
  clear channel assessment signal (carrier sense)
PMD Physical Medium Dependent
  modulation, coding
PHY Management
  channel selection, MIB
Station Management
  coordination of all management functions
PMD
PLCP
MAC
LLC
MAC Management
PHY Management
MAC
  access mechanisms, fragmentation, encryption
MAC Management
  synchronization, roaming, MIB, power management
PHY
DLC
Station Management

## Slide 20: WLAN: IEEE 802.11b
Data rate
  1, 2, 5.5, 11 Mbit/s, depending on SNR
  User data rate max. approx. 6 Mbit/s
Transmission range
  300m outdoor, 30m indoor
  Max. data rate ~10m indoor
Frequency
  Free 2.4 GHz ISM-band
Security
  Limited, WEP insecure, SSID
Availability
  Many products, many vendors
Connection set-up time
  Connectionless/always on
Quality of Service
  Typ. Best effort, no guarantees (unless polling is used, limited support in products)
Manageability
  Limited (no automated key distribution, sym. Encryption)
Special Advantages/Disadvantages
  Advantage: many installed systems, lot of experience, available worldwide, free ISM-band, many vendors, integrated in laptops, simple system
  Disadvantage: heavy interference on ISM-band, no service guarantees, slow relative speed only

## Slide 21: WLAN: IEEE 802.11a
Data rate
  6, 9, 12, 18, 24, 36, 48, 54 Mbit/s, depending on SNR
  User throughput (1500 byte packets): 5.3 (6), 18 (24), 24 (36), 32 (54)
  6, 12, 24 Mbit/s mandatory
Transmission range
  100m outdoor, 10m indoor
    E.g., 54 Mbit/s up to 5 m, 48 up to 12 m, 36 up to 25 m, 24 up to 30m, 18 up to 40 m, 12 up to 60 m
Frequency
  Free 5.15-5.25, 5.25-5.35, 5.725-5.825 GHz ISM-band
Security
  Limited, WEP insecure, SSID
Availability
  Some products, some vendors
Connection set-up time
  Connectionless/always on
Quality of Service
  Typ. best effort, no guarantees (same as all 802.11 products)
Manageability
  Limited (no automated key distribution, sym. Encryption)
Special Advantages/Disadvantages
  Advantage: fits into 802.x standards, free ISM-band, available, simple system, uses less crowded 5 GHz band
  Disadvantage: stronger shading due to higher frequency, no QoS

## Slide 22: WLAN
Advantages
  Flexibility
  Planning
  Design
  Robustness
  Cost
Disadvantages
  Quality of service
  Proprietary solutions
  Restrictions
  Safety and security

## Slide 23: WPAN
Wireless Personal Area Network where the interconnected devices are centered around a person’s workspace and connected through wireless medium
Some more examples of WPAN includes Wireless mouse, Wearable devices, USB flash drives, Digital cameras, Bluetooth, Wi-Fi, Thermostats, Security systems, Lighting controls, Motion sensors, Personal server and Leak sensors etc.

## Slide 24: WPAN Classess
High-rate WPAN (HR-WPAN) : It is defined in the IEEE 802.15.3 standard. Data throughput is > 20 Mbps.
Medium-rate WPAN (MR-WPAN) : It is defined in the IEEE 802.15.1 standard. Data throughput is 1 Mbp.
Low-rate WPAN (LR-WPAN) : It is defined in the IEEE 802.15.4 standard. Data throughput is < 0.25 Mbps.

## Slide 25
WPAN Topologies
  Star Topology
  Mesh Topology
  Cluster Tree Topology
Technologies used
  Bluetooth
  ZigBee
  Infrared

## Slide 26
A Standard for the short range wireless interconnections of electronics devices
  Special interest Group
    Original founding members: Ericsson, Intel, IBM, Nokia, Toshiba
    Added promoters: 3Com, Agere (was: Lucent), Microsoft, Motorola
    Over 2500 members
unlicensed, industrial, scientific and medical (ISM) band at 2.4 GHz to 2.485 GHz
Maximum devices 7
Bluetooth ranges upto 10 meters
data rates upto 1 Mbps or 3 Mbps
FHSS (Frequency hopping spread spectrum).

## Slide 27: Piconet
A very important term in the context of Bluetooth is a piconet. A piconet is a collection of Bluetooth devices which are synchronized to the same hopping sequence
Collection of devices connected in an ad hoc fashion
One unit acts as master and the others as slaves for the lifetime of the piconet
Master determines hopping pattern, slaves have to synchronize
Each piconet has a unique hopping pattern
Participation in a piconet = synchronization to hopping sequence
Each piconet has one master and up to 7 simultaneous slaves (> 200 could be parked)
3 bit active member address 8 bit parked member address
M=Master
S=Slave
P=Parked
SB=Standby
M
S
P
SB
S
S
P
P
SB

## Slide 28: Forming a piconet
SB
SB
SB
SB
SB
SB
SB
SB
SB
M
S
P
SB
S
S
P
P
SB



















## Slide 29: Scatternet
M=Master
S=Slave
P=Parked
SB=Standby
M
S
P
SB
S
S
P
P
SB
M
S
S
P
SB
Piconets
(each with a
capacity of
720 kbit/s)

## Slide 30: ZigBee Device Types

## Slide 31
ZigBee Co-ordinator (ZC)
  device as it forms the root of the network tree
  helps to bridge to other networks
  responsible for the start of the network.
  contains all the information of the network
  functions as a Trust Center & repository for the security keys.
ZigBee Router (ZR)
  used to route the data from other devices and help it reach the destination.
ZigBee End-Device (ZED):
  end device contains just enough functionality to talk to either the co-ordinator or the router.
  cannot rely data from other devices
  This causes the node to stay asleep for a significant time thereby increasing battery life to a considerable extent
  A ZED device requires least amount of energy as compared to the ZC or ZR.

## Slide 32: What is ZigBee Protocol?
The ZigBee wireless technology is basically a openly available global standard to address the uniques needs of low-power, low-cost wireless M2M(machine-to-machine) networks and also Internet-of-Things(IoT)
It operates on IEEE 802.15.4 physical radio specification and operates even in unlicensed band including 2.4 GHz, 900 MHz and 868 MHz.

## Slide 33
ZigBee protocol operates globally on a single frequency of 2.4 GHz.
ZigBee offers wireless range of 70m indoors and and 400m outdoors.
It offers networking flexibility to covers homes of all size by offering support for multiple networks like point-to-point, point-to-multipoint mesh-networks.
Low latency and Low Duty cycle leads to lower power consumption giving sensors the long-lasting battery life for up to 7 years.
Direct Sequence Spread Spectrum (DSSS) helps to offer higher data rate for quicker responses.

## Slide 34
Caters to thousands of devices for spread networks.
ZigBee uses AES 128 encryption (government, commercial and military grade encryption used across the Internet) thus protecting your information over the air transfers.
ZigBee can easily integrate monitoring and control of lights systems, security systems, convenience and motion detection.
The mesh-network operability of ZigBee reduces the chances of failure at nodes and the ad-hoc routing offers greater stability.

## Slide 35: WiMax
WiMax stands for Worldwide Inter-operability for Microwave Access
IEEE 802.16
provide higher data rates with increased coverage
Its range is upto 50 Km
It may provide speed upto 70 Mbps
it can operate in Non-Line-of-Sight. This technology is fast, convenient and cost effective.

## Slide 36
Physical Layer: This layer is responsible for encoding and decoding of signals and manages bit transmission and reception. It converts MAC layer frames into signals to be transmitted. Modulation schemes which are used on this layer includes: QPSK, QAM-16 and QAM-64.
MAC Layer: This layer provides and interface between convergence layer and physical layer of WiMax protocol stack. It provides point to multipoint communication and is based on CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance).
Convergence Layer: This layer provides the information of the external network. It accepts higher layer protocol data unit (PDU) and converts it to lower layer PDU. It provides functions depending upon the service being used.

## Slide 37: WiMAX Network Architecture

## Slide 38: WiMAX Network Architecture

## Slide 39: Major elements
Remote or Mobile stations: These are the user equipments that may be mobile or fixed and may be located in the premises of the user.
Access Service Network, ASN : This is the area of the WiMAX network that forms the radio access network at the edge and it comprises one or more base stations and one or more ASN gateways.
Connectivity Service Network, CSN: This part of the WiMAX network provides the IP connectivity and all the IP core network functions. It is what may be termed the core network in cellular parlance.

## Slide 40: Components
Subscriber Station, SS / Mobile Station, MS The Subscriber station, SS may often be referred to as the Customer Premises Equipment, CPE
Base Station, BS
  providing the air interface to the subscriber and mobile stations. It provides additional functionality in terms of micro-mobility management functions, such as handoff triggering and tunnel establishment, radio resource management, QoS policy enforcement, traffic classification, DHCP (Dynamic Host Control Protocol) proxy, key management, session management, and multicast group management.

## Slide 41: Components
ASN Gateway, ASN-GW
  The ASN gateway within the WiMAX network architecture typically acts as a layer 2 traffic aggregation point within the overall ASN
Home Agent, HA
  The Home Agent within the WiMAX network is located within the CSN. With Mobile-IP forming a key element within WiMAX technology, the Home Agent works in conjunction with a "Foreign Agent", such as the ASN Gateway, to provide an efficient end-to-end Mobile IP solution. The Home Agent serves as an anchor point for subscribers, providing secure roaming with QOS capabilities.

## Slide 42
Authentication, Authorisation and Accounting Server, AAA
  As with any communications or wireless system requiring subscription services, an Authentication, Authorisation and Accounting server is used. This is included within the CSN